## Slide 1: THE HISTORY OF WI-FI

## Slide 2
1971
The presentation
1973
Network standard
1985
Open network use
1988
Release of wavelan
1990
Father of wi-fi

## Slide 3
1993
1997
802.11protocol
1999
Wi-fi alliance
1999
802.11b protocol
2000
802.11a protocol
Public hotspot

## Slide 4
2003
2004
802.11i protocol
2005
802.11e protocol
2009
802.11n protocol
2014
802.11ac protocol
802.11g protocol

## Slide 5
802.11 Architecture

## Slide 6
Application
HTTP, FTP, SMTP etc.
DHCP, RTP, TFTP, etc.
TCP
UDP
IP
802.2 Logical Link Control (LLC)
802.11 Media Access Control (MAC)
Physical Layer (PHY)
(802.11b DSSS, 802.11g OFDM, 802.11n MIMO etc.)
Host
Radio

## Slide 7
Physical Layer
2.4 GHz and/or 5GHz transceiver
Spread spectrum technology
FHSS (Frequency Hopping Spread Spectrum)
DSSS (Direct Sequency Spread Spectrum)
OFDM (Orthogonal Frequecy-Division Multiplexing)
Europe: channels 1-13
USA: channels 1-11
Japan: channels 1-14

## Slide 8
Physical Layer
802.11
802.11a
802.11b
802.11g
802.11n
Standard
2.4GHz
5GHz
2.4GHz
2.4GHz
2.4/5GHz
Frequency
20
20
20
20
40
20
Bandwidth
1,2
6, 9, 12, 18, 24, 36, 48, 54
5.5,11
6, 9, 12, 18, 24, 36, 48, 54
7.2, 14.4, 21.7, 28.9, 43.3, 57.8, 65, 72.2
Symbol rate (Mb/s)

## Slide 9
Media Access Control (MAC)
Function | Explanation
Scanning | Scanning of access points. Both active (probe) and passive (beacon) scanning are provided by the standard.
Authentication | Authentication is the process of proving identity between the client and the access point.
Association | Once authenticated, the client must associate with the access point before sending data frames.
Encryption | Encryption of payload
RTS/CTS | The optional request-to send and clear-to-send (RTS/CTS) function allows the access point to control use of the medium for stations activating RTS/CTS.
Power Save Mode | The power save mode enables the user to turn on or off enables the radio.
Fragmentation | The fragmentation function enables an 802.11 station to divide data packets into smaller frames.

## Slide 10
Logical Link Control (LLC)
The LLC provides end-to-end link control over 802.11-based wireless LAN
LLC services:
Unacknowledged connectionless service
Connection-oriented service
Acknowledged connectionless service

## Slide 11
Application
HTTP, FTP, SMTP etc.
DHCP, RTP, TFTP, etc.
TCP
UDP
IP