## Slide 1: IOT102 PROJECT
Topic 1 - Automatic fire alarm system
use heat, smoke and gas sensors
Nguyen Tuan Anh
SE150633
Nguyen Tran Phong
SE150974
Vo Van Thanh Phuc
SE150980

## Slide 2: CONCLUSION & DEVELOPMENT DIRECTIONS DESIGN & IMPLEMENTATION INTRODUCTION 01 02 CONTENTS 03
DEMONSTRATION
04

## Slide 3: 1. INTRODUCTION
5000 fire incidients nation-wide
Annual Report of Vietnam’s Police Department of Fire Prevention and Fighting and Rescue in 2020
Civilian-related
75
casualties
Chart: 
| Electrical Malfunctions | Misuse of Heat and Fuel sources | Other
Percent | 0.6 | 0.25 | 0.15
Electrical Malfunctions
60%
Misuse of Heat and Fuel sources
25%

## Slide 4: 1. INTRODUCTION
Scalability
Simplicity
Cost-efficiency
Effectiveness

## Slide 5: 1. INTRODUCTION
Environments where fire is least expected to combust
Fire Sensors
Heat Sensors
Gas Source
Gas Sensors
A fire is detected within the specified range
Temperature increased exceeded the designated value
Gas concentration exceeds the safe recommended value of 1000ppm
ALARM
TRIGGER
Built-in RESET Button on the Arduino
Deactivating the Power Supply
DISABLE
ALARM

## Slide 6: 2. DESIGN & IMPLEMENTATION
Wiring connectivity

## Slide 7: 2. DESIGN & IMPLEMENTATION
Household implementation

## Slide 8: 2. DESIGN & IMPLEMENTATION

## Slide 9: 3. CONCLUSION & DEVELOPMENT DIRECTIONS
The system worked as intended.
Flame detected within an acceptable distance.
Preempt most situations, which can, at times, lead to false alarms.
Gas leakage detection is dependent on external factors such as winds and humidity. Requires further calibrations.
Alarm bell is dependent on the main power source to operate, no backup power due to cost limitation. Requires further subsidiary.
The fire sensor does not cover a comparatively wide angle.

## Slide 10: 3. CONCLUSION & DEVELOPMENT DIRECTIONS
DECISION FLOWCHART
System started
Continuously measure the environment
Gas
detected
Temperature
exceeds
threshold
Fire detected
Alarm is activated
User
disables
alarm
User
disables
system
System terminated
Yes
Yes
Yes
No

## Slide 11: 3. CONCLUSION & DEVELOPMENT DIRECTIONS
PSEUDO CODE
lcd.start();
defaultTempThreshold = read(potentiometed);
while(systemNotTerminated){
  lcd.display(defaultTempThreshold);
  currentGas = read(gasSensor);
  currentTemp = read(heatSensor);
  currentFire = read(fireSensor);
  lcd.display(currentTemp);
  if(currentGas == true){
  alarm();
  }
else if(currentTemp >= defaultTempThreshold){
alarm();
}
else if(currentFire == true){
alarm();
}
}

## Slide 12: 3. CONCLUSION & DEVELOPMENT DIRECTIONS
SOURCE CODE
#include "LiquidCrystal_I2C.h"
const int DANGEROUS_GAS = 1000;
int interval = 1000;
int potPinDef = A3;
int defHeatValue;
int gasPin = A0; int gasValue;
int firePin = 2; int fireValue;
int heatPin = A1; int heatValue;
int bellPin = 4;
//Create the LCD object
LiquidCrystal_I2C lcd(0x27, 16, 2);
void setup() {
    pinMode(firePin,INPUT);
    //Set up the LCD's rows and columns
    lcd.init();
    lcd.backlight();
    //Activate bell's digital pin
    pinMode(bellPin,OUTPUT);
    lcd.print("Welcome! Welcome!");
    delay(interval);
}

## Slide 13: 3. CONCLUSION & DEVELOPMENT DIRECTIONS
SOURCE CODE
#include "LiquidCrystal_I2C.h"
const int DANGEROUS_GAS = 1000;
int interval = 1000;
int potPinDef = A3;
int defHeatValue; int defGasValue;
int gasPin = A0; int gasValue;
int firePin = 2; int fireValue;
int heatPin = A1; int heatValue;
int bellPin = 4;
//Create the LCD object
LiquidCrystal_I2C lcd(0x27, 16, 2);
void alarm(){
digitalWrite(bellPin,HIGH);
delay(3000);
digitalWrite(bellPin,LOW);
}

## Slide 14: 3. CONCLUSION & DEVELOPMENT DIRECTIONS
SOURCE CODE
#include "LiquidCrystal_I2C.h"
const int DANGEROUS_GAS = 1000;
int interval = 1000;
int potPinDef = A3;
int defHeatValue; int defGasValue;
int gasPin = A0; int gasValue;
int firePin = 2; int fireValue;
int heatPin = A1; int heatValue;
int bellPin = 4;
//Create the LCD object
LiquidCrystal_I2C lcd(0x27, 16, 2);
void displayTemp(int reading){
delay(interval);
lcd.clear();
//Set the LCD to start displaying on the first row
lcd.setCursor(0,0);
//Display the threshold value
lcd.print("THRESHOLD(C):");
lcd.print(defHeatValue);
//Set the LCD to start displaying on the second row
lcd.setCursor(0,1);
  //Print out current temperature
  lcd.print("CURRENT(C):");
  lcd.print(reading);
  //Room's temperature exceeds specified value
  if(reading > defHeatValue){
  lcd.setCursor(0,0);
  lcd.print("MAXIMUM EXCEEDED!");
  alarm();
  }
}

## Slide 15: 3. CONCLUSION & DEVELOPMENT DIRECTIONS
SOURCE CODE
#include "LiquidCrystal_I2C.h"
const int DANGEROUS_GAS = 1000;
int interval = 1000;
int potPinDef = A3;
int defHeatValue; int defGasValue;
int gasPin = A0; int gasValue;
int firePin = 2; int fireValue;
int heatPin = A1; int heatValue;
int bellPin = 4;
//Create the LCD object
LiquidCrystal_I2C lcd(0x27, 16, 2);
void displayGas(int reading){
delay(interval);
lcd.clear();
//No gas leakage yet
if(reading < DANGEROUS_GAS){
lcd.setCursor(0,0);
lcd.print(" NORMAL STATUS");
}
//Gas leakage exceeds the recommended level
else if(reading >= DANGEROUS_GAS){
lcd.setCursor(0,0);
lcd.print(" GAS DETECTED!");
alarm();
}
}

## Slide 16: 3. CONCLUSION & DEVELOPMENT DIRECTIONS
SOURCE CODE
#include "LiquidCrystal_I2C.h"
const int DANGEROUS_GAS = 1000;
int interval = 1000;
int potPinDef = A3;
int defHeatValue; int defGasValue;
int gasPin = A0; int gasValue;
int firePin = 2; int fireValue;
int heatPin = A1; int heatValue;
int bellPin = 4;
//Create the LCD object
LiquidCrystal_I2C lcd(0x27, 16, 2);
void displayFire(int reading){
delay(interval);
lcd.clear();
//No fire detected
if(reading == 0){
lcd.setCursor(0,1);
lcd.print(" NO FLAME");
}
//A fire's IR is sufficient to decrease the sensor's thermal resistance
else{
lcd.setCursor(0,1);
lcd.print("FLAME DETECTED");
alarm();
}
}

## Slide 17: 3. CONCLUSION & DEVELOPMENT DIRECTIONS
SOURCE CODE
#include "LiquidCrystal_I2C.h"
const int DANGEROUS_GAS = 1000;
int interval = 1000;
int potPinDef = A3;
int defHeatValue; int defGasValue;
int gasPin = A0; int gasValue;
int firePin = 2; int fireValue;
int heatPin = A1; int heatValue;
int bellPin = 4;
//Create the LCD object
LiquidCrystal_I2C lcd(0x27, 16, 2);
void loop() {
lcd.clear();
//Read the default thresholds, adjustable with the potentiometer
defHeatValue = (analogRead(potPinDef)*5.0/1024)*100;
//Read the MQ2's sensor values
gasValue = analogRead(gasPin);
//Read the fire sensor values
fireValue = digitalRead(firePin);
//Read the heat sensor values
heatValue = (analogRead(heatPin)*5.0/1024)*100;
displayTemp(heatValue);
displayGas(gasValue);
displayFire(fireValue);
delay(interval);
}

## Slide 18: 4. DEMONSTRATION

## Slide 19: REFERENCES
Vietnamese Police Department of Fire Prevention and Fighting and Rescue. (2020). Annual report regarding the process of fire prevention, fighting, and rescue of 2020. Retrieved from: http://canhsatpccc.gov.vn/ArticlesList/tabid/192/cateid/1172/language/vi-VN/default.aspx
Đ.V. Mạnh. (2018). Vietnam’s state of fire incidents in recent years, and preemptive measures to be applied. Retrieved from: http://csnd.vn/Home/Nghien-cuu-Trao-doi/3983/Tinh-hinh-chay-no-o-Viet-Nam-trong-nhung-nam-gan-day-va-mot-so-giai-phap-phong-ngua-ngan-chan
Seeed. (2020). Grove - Gas Sensor (MQ2). Retrieved from: https://wiki.seeedstudio.com/Grove-Gas_Sensor-MQ2/
Proctor NH, Hughes JP, Fischman ML [1988]. Liquified petroleum gas. In: Chemical hazards of the workplace. 2nd ed. Philadelphia, PA: J.B. Lippincott Company, pp. 301, 420-421.

## Slide 20: THANK YOU FOR YOUR ATTENTION